## Slide 1: Distributed Computing Internet of Things (IoT)
Dr. Barsha Mitra
CSIS Dept, BITS Pilani, Hyderabad Campus

## Slide 2
IoT for Ubiquitous Computing
IoT is a natural extension of the Internet
foundation of IoT is radio-frequency identification (RFID)
RFID enables discovery of tagged objects and mobile devices by browsing an IP address
objects include electronic devices, humans, animals, food, clothing, homes, vehicles, commodities, trees, hills, landmarks

## Slide 3
Enabling and Synergistic Technologies
supportive technologies are divided into 2 categories:
  enabling technologies –
    build up the foundations of IoT
    eg., - tracking (RFID), sensor networks, GPS
  synergistic technologies –
    play supporting roles
    eg., - biometrics, artificial intelligence, computer vision, robotics, telepresence

## Slide 4
Architecture of the Internet of Things
3-layer architecture
top layer: consists of applications
bottom layers: represent various types of sensing devices like RFID tags, ZigBee or other types of sensors, and road-mapping GPS navigators
signals or information collected at these sensing devices are linked to the applications through the cloud computing platforms at the middle layer
sensors and filters are used to collect raw data
compute and storage clouds and grids process the data and transform it into information and knowledge formats
sensed information is put together for a decision-making system

## Slide 5
Architecture of the Internet of Things

## Slide 6
Radio-Frequency Identification (RFID)
RFID is applied with electronic labels or RFID tags on any object being monitored or tracked
identify and track objects using radio waves or sensing signals
Components of RFID h/w
  RFID tag - tiny silicon chip attached to a small antenna
  2 major parts
    integrated circuit for storing and processing information, modulating and demodulating radio-frequency (RF) signal etc.
    antenna for receiving and transmitting radio signals

## Slide 7
Radio-Frequency Identification (RFID)
Components of RFID h/w
  Reader antenna –
    used to radiate energy and then capture the return signal sent back from the tag
    integrated with a handheld reader device or connected to the reader by cable
  Reader –
    device station that talks with the tags
    may support one or more antennae

## Slide 8
Types of RFID Tags
  active RFID tags containing a battery and transmitting signals autonomously
  passive RFID tags have no battery and require an external source to induce signal transmission
  battery-assisted passive RFID tags require an external source to wake up the battery

## Slide 9
Smart Buildings
enhance our lives with comfort, convenience, and security
reduce energy costs and environmental impacts
may include alarm systems, access controls, indoor climate controls, elevators
smart building - shopping mall, home, hospital, high-rise office tower
need monitoring and regulation of heating, air conditioning, lighting, and environmental changes
can oversee building security, fire suppression, and elevator operations
smart building technologies focus on bringing more detailed monitoring and sensing “awareness” to buildings

## Slide 10
Smart Buildings

## Slide 11
References
Kai Hwang, Geoffrey C. Fox, and Jack J. Dongarra, “Distributed and Cloud Computing: From Parallel processing to the Internet of Things”, Chapter 9.
https://www.exchangecommunications.co.uk/products/smart-building-and-cities/smart-buildings.php
https://blog.econocom.com/en/blog/smartbuilding-and-bms-a-little-glossary/
https://www.security-warehouse.com/rfid-iot/rfid-antenna.html
https://www.scnsoft.com/blog/iot-for-inventory-management
https://www.autodesk.com/products/eagle/blog/rfid-works-antenna-design/

## Slide 12
Thank You